## Slide 1: Exceeding 1012 D-D neutrons/shot from 1 MJ Dense Plasma Focus FAETON-X
Sing Lee*, Vahid Damideh*, JC Btaiche, Isaac Hassen, Sophie Faliero
Fuse Energy Technologies Corp., San Leandro, CA, USA
Fuse Energy Technologies Inc., Napierville, QC, Canada
*E-mail: leesing111@yahoo.com
To be presented at ISVSP/ICPSA, Batangas City, Philippines, September 16-18, 2026

## Slide 2: The 50-Year Problem - Myth of Saturation
Notable large and MA-class Dense Plasma Focus DPF:
SPEED 2, Poseidon, the Frascati 1 MJ, DPF 6.5, PF-1000, Gemini , Sodium (ZEUS) and Verus DPF.
Published: D-D neutron yields 1.2E11 - 4.8E11 n/pulse; MA/MJ 2.35 to 3.25.
1974: LANL DPF6.5, 0.72 MJ, 2.2 MA = 1.2E12 DD (claimed)
2024: MJOLNIR, LLNL, 1.3 MJ, 3.8 MA = 1.2E12 DD (published)
50 YEARS to equal the record -> belief of SATURATION
Result: Cancellation of large focus projects (USSR, Europe, USA)
2009 Lee: APL 95 151503 - Misnomer, not saturation, but arithmetics of diminishing returns- total impedances tending to load impedance as capacitances become increasingly larger, exceeding hundreds of mF.
Cure: Increase operational voltage -> Faeton X design principle
FX also has the highest current energy efficiency of 4.5 MA/MJ

## Slide 3: Operating under time matched conditions: Lee code yields the following scaling
The neutron yield of a DPF scales Yn = 1.8 × 1010 Ipeak3.8 Ipeak is in MA.
.

## Slide 4: - Indications that FX will Recover Scaling
Faeton X - Highest current efficiency MA PF’s: 4.5 MA /MJ
Three enabling conditions:(a) High voltage: 65 kV operation(b) Fast synchronized multi-module triggering(c) Reduced inductance
Diagnostics: photodiodes, PCDs, B-dots, nToF, In-foil, bubble detectors
Key indicator: Dynamically-induced voltage pulse peaks >400 ns BEFORE pinch - sharpens with conditioning
Integrated analysis of diagnostics with Lee Code

## Slide 5: - New Record: 1.8E12/Shot
14 Aug 2026 - : 65 kV, 1 MJ, 4.5 MA -> 1.8 x 10^12 DD neutrons (Bubble detectors confirmed by integrated analysis)
EXCEEDS PF DD RECORD 1.2E12 set 52 years ago
Consistency:
Series of 10 shots: avg 1.02E12 - surpasses design goal 5E11
Effective current fraction fc is only 0.52, should progress towards typical value of 0.7; then will optimize yield at higher pressure to reach scaled yield of 5E12.

## Slide 6: FX: Fig. 1 (a) view showing diagnostic layout: (1) photodiode array, (2) photodiode 1, (3) PCD 1, (4) PCD 2, and (5) B-Dot probes; and (b) cross-sectional view of the D-T

## Slide 7: Fuse FX: Design & operational characteristics
Anode radius 15 cm
Cathode radius 21 cm
Cathode length 61.5 cm
Effective anode length 41.2 cm
Insulator sleeve length 9 cm
Insulator sleeve thickness 1.5 cm
System capacitance 500 μF
Capacitor bank energy 1 MJ
Operating voltage 65 kV
Static inductance ∼55 nH
Operating gas D2, D2+Kr, D2+T2
Operating gas pressure 1-20 Torr
Peak current 5 MA

## Slide 8: Measured Neutrons per shot

## Slide 9: Various Diagnostics

## Slide 10: Lee Code Validation - Shot #245; 1.8E12 measured, verified by integrated analysis
Lee Code configured to FX geometry & bank, fitted to measured current; check against measured voltage (excellent agreement), computed axial & radial dynamics
Fit parameters: current fraction fc = 0.52, mass swept fm=0.15, Results: Yn = 1.7E12 vs 1.8E12 measured - beam-target origin

## Slide 11: Integrated analysis: correlation of code with diagnostics enable to identify & optimise mechanism for fast ion beam production

## Slide 12: Examine the Details of the radial phase

## Slide 13: Road to 5E12 DD
Present fc = 0.52
As series progresses expect effective current fraction to improve towards 0.7 of typical well-conditioned DPF; can operate at higher pressure
Projection: Yn = 5E12 DD (properly scaled yield).
This will CLEARLY dispel myth of saturation, confirm non-saturation of scaling

## Slide 14: FX Engineered for DT Peak reactivity
DD: dynamic voltage spike driving D+ ~150 kV at 10 Torr
DT: would scale to 115 kV at ~15Torr
Hit peak of D-T cross-section
Gain of more than 100x
Fine tuning pressure and charging voltage, expect go beyond 5xE14 D-T neutrons

## Slide 15: Faeton X projection
FX: present: consistent E12/shot; best 1.8E12
Expect progression to best 5E12 DD.
Switch to D-T, tune pressure, operational voltage to hit dynamically induced peak voltage of 115 kV to reach > 5E14 neutrons/shot.
From SAME 1 MJ Faeton X - no new machine, just switch gas to D-T 50:50. >5E14 from 1 MJ DPF redefines compact fusion neutron source
Applications: fusion research and radiation-effects, laboratory-scale evaluation of electronics, materials, and components against displacement damage, single-event effects, and dose-rate phenomena that would otherwise require reactor irradiation or underground nuclear testing; positioning the FX platform as a compact, controllable fast-neutron source for survivability qualification and radiation-hardness assurance..

## Slide 16: Yield Progression (DPF) extended by FX …& a glimpse beyond of FUSE
LANL 1974 1.2E12
MJOLNIR 2024 1.2E12
FX DD Aug 2026 1.8E12
FX DD projected 5E12
FX DT projected E15
A glimpse of FUSE (development of MAGLIF systems):
www.f.energy: MAGLIF systems, Z-Star, Apeiron: E18-E21
Vacuum 216 (2023) 112471; S Lee, V Damideh, JC Btaiche
“MagLIF: Dynamics and energetics of liner and fuel“

## Slide 17: Faeton X (FX) facility at Fuse Energy Technologies

## Slide 18: Conclusion
FX has exceptional current efficiency: of 4.5 MA/MJ,
FX has well-defined plasma structures and dynamics validating the correlation of measured and simulated results for effective integrated analysis.
Consistent series of e.g.10 shots averaging 1.02E12, best measured yield of 1.8x1012 - exceeding the record of 1.2x1012 set 52 years ago.
Shots statistics continue improving. The current fraction fc driving the critical processes is expected to improve from its present 0.52 towards 0.7, allowing higher pressure operation to reach the scaled yield of 5x 1012 ; which will clearly dispel the myth of neutron saturation.
An exciting feature of FX: fast ion beams are close to 115 keV, peak of D-T reactivity- facilitates production of D-T neutrons approaching 1015/shot.

## Slide 19: Thank You- Questions
Acknowledgements: FUSE Team,